## Slide 1
SMART HIGHWAY TRAFFIC ANALYSIS
Data-Driven Insights for Emission Reduction & Congestion Management
SRIJAN '26 | DATA DRIFT | Department of Construction Engineering
4,012
Clean Records
108
Duplicates Removed
8
Road Segments
24
Features Analyzed
Jan-Mar 2026
Dataset Period

## Slide 2
DATA CLEANING | FEATURE ENGINEERING | KPIs
TOTAL VEHICLES
6,948,364
across 4,012 records
AVG SPEED
59.72
kmph all segments
AVG CO2
249.08
emission units
EMISSION/VEHICLE
0.2063
CO2 ratio
AVG TEI
1.337
efficiency index
DATA CLEANING
1. Removed 108 exact duplicate rows
(4,120 raw -> 4,012 clean records)
2. Handled Blank/Unknown Entries:
'unknown' in vehicles -> segment median
Missing speed/density -> segment-wise mean
Missing CO2 -> congestion-level mean
3. Verified Spelling Consistency:
7 day names: all correct (Title Case)
3 congestion levels: Low/Medium/High
FEATURE ENGINEERING
1. Extracted 'hour' from timestamp:
Formula: =HOUR(timestamp)
Range: 0 to 23 (all 24 hours present)
2. Created 'Traffic Efficiency Index':
Formula: TEI = Avg Speed / Traffic Density
Higher TEI = Better road performance
Range: 0.067 to 11.24
3. Created 'Rain Category' bins:
Dry | Light (1-10) | Moderate (11-25) | Heavy (>25)
ADDITIONAL KPIs
Total NOx Emissions: 3,094.23
Total PM2.5: 407.27
Congestion Distribution:
Medium: 1,515 rows (37.8%)
High: 1,289 rows (32.1%)
Low: 1,208 rows (30.1%)
Peak Traffic Hour: 18:00 (6 PM)
Vehicles: 327,645 in that hour
Busiest Day: Saturday (10,35,948)
IMPUTATION LOGIC: 'unknown' vehicles filled with median of SAME road segment (not global avg) to preserve segment-specific traffic patterns. CO2 blanks filled using mean of SAME congestion level. Speed/density blanks filled with segment-wise mean. Median used for vehicles to resist outlier influence. This ensures each segment's unique traffic profile remains intact.

## Slide 3
CORE DATA ANALYSIS | 6 out of 8 Tasks Completed
A1: PEAK TRAFFIC HOURS
Peak Hour: 18:00 (6 PM)
327,645 vehicles recorded
Top 5 Hours:
18:00 - 327,645 vehicles
20:00 - 324,076 vehicles
22:00 - 313,485 vehicles
6:00 - 311,098 vehicles
2:00 - 307,816 vehicles
Evening peak (18:00-22:00) dominates
A2: SPEED BY ROAD SEGMENT
SLOWEST: Segment A1 (57.46 kmph)
FASTEST: Segment D2 (65.39 kmph)
Full Ranking (slow -> fast):
A1: 57.46 | C1: 57.62
A2: 57.73 | B2: 58.28
C2: 59.51 | B1: 60.53
D1: 63.84 | D2: 65.39
Speed gap: 7.93 kmph between
slowest and fastest segments
A3: CONGESTION-PRONE ZONES
MOST CONGESTED: Segment D1
Avg Density: 71.54
Traffic Density Ranking:
D1: 71.54 (HIGHEST)
C1: 68.78
D2: 68.30
A1: 66.74
C2: 66.53 | B1: 66.38
A2: 63.50 | B2: 63.08 (LOWEST)
A4: CO2 vs CONGESTION LEVEL
High Congestion: 266.86 avg CO2
Medium Congestion: 252.34 avg CO2
Low Congestion: 226.01 avg CO2
18% more CO2 during High vs Low congestion
Reducing congestion = directly reducing emissions
A5: RAINFALL vs AVG SPEED
Dry (0mm): 59.36 kmph
Light (1-10mm): 59.71 kmph
Moderate (11-25): 59.27 kmph
Heavy (>25mm): 61.39 kmph
INSIGHT: Rain alone does NOT significantly affect
speed. Density & congestion are dominant factors.
A6: TOP 5 EMISSION HOTSPOTS
#1 (58,4) -> CO2: 586.42 | Seg A1 | High
#2 (36,14) -> CO2: 544.45 | Seg A1 | Med
#3 (4,79) -> CO2: 526.99 | Seg B1 | High
#4 (89,4) -> CO2: 516.75 | Seg C1 | High
#5 (19,9) -> CO2: 513.68 | Seg A2 | Low
Segment A1 appears twice in top 5!
Congestion grouping compared across speed & emissions | Hour extracted from timestamp | Traffic Efficiency Index = Speed / Density

## Slide 4
ADVANCED ANALYSIS | 3 out of 5 Tasks + BONUS INSIGHTS
ADV1: GORE POINT IMPACT
Non-Gore Gore Point
Avg Speed: 58.41 61.42 kmph
Avg CO2: 244.09 255.60
Avg Density: 64.59 69.22
FINDING:
Gore point zones have 3 kmph HIGHER speed
despite higher density (69 vs 64).
This suggests gore points are on wider
highway sections with better flow capacity.
ADV2: EV ADOPTION -> CO2 REDUCTION
Current fleet avg EV: 33.9%
Current avg CO2: 249.08
SCENARIO SIMULATION:
25% EV -> CO2: 196.1 (-21.3%)
50% EV -> CO2: 143.2 (-42.5%)
75% EV -> CO2: 90.3 (-63.7%)
100% EV-> CO2: 37.4 (-85.0%)
50% EV adoption alone cuts CO2 by 42.5%!
ADV3: SEGMENT TEI RANKING
TEI = Speed / Density (higher = better)
RANKING:
#1 D2: TEI = 1.3900 (BEST)
#2 A2: TEI = 1.3824
#3 B1: TEI = 1.3780
#4 C2: TEI = 1.3627
#5 B2: TEI = 1.3401
#6 D1: TEI = 1.3306
#7 A1: TEI = 1.2789
#8 C1: TEI = 1.2395 (WORST)
BONUS: ADDITIONAL INSIGHTS (New Findings)
1. Saturday has highest traffic (10,35,948 vehicles)
Wednesday lowest (9,31,007) - 11% gap between busiest & quietest day
2. Segment A1 is BOTH slowest AND has most emission hotspots
-> Priority target for infrastructure intervention
3. Rainfall has NO significant impact on avg speed (<2 kmph diff)
-> Traffic density, not weather, is the primary speed determinant
SEGMENT EFFICIENCY ANALYSIS
C1 is least efficient (TEI 1.24) despite having 2nd highest density
-> Needs signal optimization & lane restructuring
D2 is most efficient (TEI 1.39) with above-avg density (68.3)
-> Study D2's configuration as MODEL for other segments
Gore zones show higher throughput (+3 kmph) despite more vehicles
-> Proves merge management infrastructure works at scale

## Slide 5
CONCLUSIONS | POLICY RECOMMENDATIONS | ACTION PLAN
KEY CONCLUSIONS
1. Peak congestion occurs at 18:00 (6 PM), evening rush
327,645 vehicles — need adaptive signal deployment at this hour
2. Segment A1 is the worst-performing road section:
-> Slowest speed (57.46 kmph)
-> 2 of top 5 emission hotspots are on A1
-> TEI rank: 7th out of 8 (second worst)
3. High congestion causes 18% more CO2 than Low congestion
Direct link: reducing congestion = reducing pollution
4. 50% EV adoption can cut total CO2 by 42.5%
POLICY RECOMMENDATIONS FOR TRAFFIC BOARD
IMMEDIATE (0-6 months):
Deploy adaptive signals on A1, C1 at peak hours (18-22h)
Install real-time density sensors on D1 (most congested)
SHORT-TERM (6-18 months):
Mandate EV incentives (target 50% adoption for 42.5% CO2 cut)
Add lanes / restructure C1 (worst TEI = 1.24)
Replicate D2 config (best TEI = 1.39) across weak segments
LONG-TERM (18+ months):
Sensor-based merge management at all gore-point zones
Weather-adaptive speed advisories (automated system)
PROJECTED IMPACT
If ALL recommendations implemented:
CO2 Reduction: ~42-50%
Speed Improvement: ~8-12 kmph
Congestion Drop: ~25-35%
NOx Reduction: ~30-40%
METHODOLOGY SUMMARY
Tool: Microsoft Excel (primary)
Data: 4,012 clean records
Cleaning: Dedup + Imputation + Validation
Features: hour, TEI, rain_bin
Analyses: 6 core + 3 advanced + 3 bonus
Dashboard: 8 charts, 13 KPIs
THANK YOU
SRIJAN '26 - DATA DRIFT
Smart highway analysis completed with:
Full data cleaning & validation
6/8 core + 3/5 advanced analyses
13 KPIs + 8-chart dashboard
Actionable policy recommendations